## Slide 1: CS118 Assembly Language
Chapter 4
More on Intel Arithmetic and Logic Operations

## Slide 2: Section 1
Multiplication and Division

## Slide 3: Multiplication 01

## Slide 4: Multiplication
If you multiply two numbers, you are likely to get an answer with more digits
For example, 9x6 = 54
9 has one digit, 6 has one digit, but the result has two digits
We have the same problem on a computer
This presents a problem

## Slide 5: The Problem
Pretend these numbers are decimal
Of course, they are binary numbers, but the ideas are the same
What if
  ah contains 1000 0000
  al contains 1000 0000
The product is 100 0000 0000 0000
This is not just a few digits bigger than either of those registers, it’s a lot bigger

## Slide 6: The IMUL Instruction
The IMUL instruction with 16 bit operands looks like this
  imull %bx
Wait--It seems that a lot of pieces are missing!
bx is multiplied by something, but what?
Where does the result go?

## Slide 7: Examining the IMUL instruction
The IMUL instruction multiplies something by ax
So now we know the operation is ax * bx
How about the result?
  The result goes into dx:ax
That means that we treat the dx register as placed to the left of the ax register
  We now have 32 bits
And we treat that like one long 32-bit doubleword

## Slide 8: An Example
Let’s multiply 2500010 by 410
  The hardware does this in binary, but I will do it in hex
Suppose bx contains 2500010
Suppose ax contains 410
The product is, of course, 10000010
  2500010 = 61A816
  410 = 416

## Slide 9: Looking into the Hardware
61A816 * 416 = 186A016
So, dx contains 1 and ax contains 86A0(hex)
  86A016 = 3446410
You can convert these numbers to decimal and check the answer
Remember, to convert dx:ax to decimal, you multiply dx by 65536 and add it to ax

## Slide 10: A Multiplication Table for Hex Math
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F
2 | 0 | 2 | 4 | 6 | 8 | A | C | E | 10 | 12 | 14 | 16 | 18 | 1A | 1C | 1E
3 | 0 | 3 | 6 | 9 | C | F | 12 | 15 | 18 | 1B | 1E | 21 | 24 | 27 | 2A | 2D
4 | 0 | 4 | 8 | C | 10 | 14 | 18 | 1C | 20 | 24 | 28 | 2C | 30 | 34 | 38 | 3C
5 | 0 | 5 | A | F | 14 | 19 | 1E | 23 | 28 | 2D | 32 | 37 | 3C | 41 | 46 | 4B
6 | 0 | 6 | C | 12 | 18 | 1E | 24 | 2A | 30 | 36 | 3C | 42 | 48 | 4E | 54 | 5A
7 | 0 | 7 | E | 15 | 1C | 23 | 2A | 31 | 38 | 3F | 46 | 4D | 54 | 5B | 62 | 69
8 | 0 | 8 | 10 | 18 | 20 | 28 | 30 | 38 | 40 | 48 | 50 | 58 | 60 | 68 | 70 | 78
9 | 0 | 9 | 12 | 1B | 24 | 2D | 36 | 3F | 48 | 51 | 5A | 63 | 6C | 75 | 7E | 87
A | 0 | A | 14 | 1E | 28 | 32 | 3C | 46 | 50 | 5A | 64 | 6E | 78 | 82 | 8C | 96
B | 0 | B | 16 | 21 | 2C | 37 | 42 | 4D | 58 | 63 | 6E | 79 | 84 | 8F | 9A | A5
C | 0 | C | 18 | 24 | 30 | 3C | 48 | 54 | 60 | 6C | 78 | 84 | 90 | 9C | A8 | B4
D | 0 | D | 1A | 27 | 34 | 41 | 4E | 5B | 68 | 75 | 82 | 8F | 9C | A9 | B6 | C3
E | 0 | E | 1C | 2A | 38 | 46 | 54 | 62 | 70 | 7E | 8C | 9A | A8 | B6 | C4 | D2
F | 0 | F | 1E | 2D | 3C | 4B | 5A | 69 | 78 | 87 | 96 | A5 | B4 | C3 | D2 | E1

## Slide 11: An Example
Suppose I wanted to multiply x by 15
I would do this
  movw $15, %bx
  movw x, %ax
  imulw %bx
After this, dx:ax contains 15*x

## Slide 12: Signed Multiplication
What if we convert -1 to two’s complement?
  We use 8 bits (total), with one sign bit
Let’s copy that into a 16 bit word
Oops. It’s not -1 anymore, it’s +255
We have to extend the sign:
  We fill the left byte with 1s
Extending the sign means
  When copying data to a larger space, the extra bits to the left get filled with the sign with the sign

## Slide 13: imul Is Signed Multiplication
This is something to watch for
imul does it correctly, but you may have to check dx for sign information
Remember, the result is in the full dx:ax
There is also the instruction MUL
MUL is unsigned
Otherwise, MUL is like IMUL

## Slide 14: How about 32 Bit Multiplication?
It’s very similar
The combination edx:eax gets the result of eax times the operand of the IMUL instruction

## Slide 15: Division 02

## Slide 16: Division vs. Multiplication
We will focus on integer division
Now we have the opposite problem
100 (a three-digit number) divided by 25 (a two-digit number) = 4 (a one-digit number)
The quotient may have fewer digits than the original number
  It’s called the dividend
  It’s 100 in our case

## Slide 17: There’s More!
20 / 7 = 2 with a remainder of 6
It would be nice if we could get the quotient (which is 2) AND the remainder (which is 6)
You guessed it—we can!
You put 20 into dx:ax (Be careful here!)
You put 7 into bx
You execute: IDIVW %bx
The quotient is in ax; the remainder is in dx

## Slide 18: Division Itself
We start with a number in dx:ax
We divide by the operand of
  IDIV operand
The quotient goes into ax
The remainder goes into dx
Let’s try that with an example

## Slide 19: An Example for Division
Suppose
  dx contains 0
  ax contains 3010, which is 1E16
x is a word variable that contains 4
We execute idivw x
dx contains 2
ax contains 7

## Slide 20: Signs!
Like imul, this is signed division
This could be a problem
If you are only dividing by what’s in ax, you need to sign extend it into dx
The book does this by putting
  -1 into dx if the number in ax is negative
    -1 is all 1s in bits
  0 into dx if the number in ax is positive

## Slide 21: Section 2
Carry and Overflow

## Slide 22: Signed Math 01

## Slide 23: Signed Math
Remember, Intel hardware uses twos complement to store negative numbers
This causes two issues
I will illustrate them with 5 bits
  One bit is the sign bit
  The other four bits are data bits

## Slide 24: Issue 1: Overflow
This happens when you add two positive number and get a negative answer
For example, let’s add 1210 and 1210
Wait! Run that by me again

## Slide 25: What Happened
The hardware doesn’t know it’s in the two’s complement world
It just adds bits
We were wearing our glasses the day we programmed this and knew 12 was +12
We also knew that if you add two positive numbers, you can’t get a negative number
This is an example of overflow

## Slide 26: What about Adding Negative Numbers?
There is a similar situation for negative numbers
If you add two negative numbers and the result is positive, the overflow flag is set

## Slide 27: Issue 2:
Let me try again
Let’s add 15 and 1
This time I will assume the numbers are unsigned
So, let’s assume we have 4 data bits

## Slide 28: An Example
What? 15 + 1 = 0?

## Slide 29: The Carry Bit
The carry bit is set every time there is a carry out of the leftmost bit position

## Slide 30: The Moral of the Story
If you are doing signed arithmetic
  Check the overflow flag for errors
    Ignore the carry flag
If you are doing unsigned arithmetic
  Check the carry flag for errors
    Ignore the overflow flag

## Slide 31: Section 3
Logical Operations

## Slide 32: The AND instruction 01

## Slide 33: AND Logic
AND means the same as & in C++
& is similar to &&
  && checks for a condition
  & is an operator, like + or –
If you are used to &&, you know its rules
  && is true only when the expressions on both sides are true

## Slide 34: Interpreting This in Bits
1 means true and 0 means false
So interpreting this in terms of &&
  0 AND 0 = 0
  0 AND 1 = 0
  1 AND 0 = 0
  1 AND 1 = 1

## Slide 35: Doing This for Bits
We can extend this idea to many bits
Let’s use a 4-bit example
Let’s try to do this example

## Slide 36: The Takeaway for AND
The key items to notice for AND is this
0 AND 0 = 0 0 AND 1 = 0
1 AND 0 = 0 1 AND 1 = 1
Notice
  ANYTHING AND 0 = 0
  ANYTHING AND 1 = itself
This means that
  ANDing against 0 changes bits to 0
  ANDing against 1 keeps bits the same

## Slide 37: Clearing Bits
This makes it easy to clear specific bits in storage
  Clearing a bit means setting it to 0
  You can clear bits in a byte, word, …
To do this, you create a mask
  You AND the mask against the data
  It keeps the bits you want
  It sets the other bits to 0
The mask has
  1s for bits you don’t want to change
  0s for bits you want to set to 0

## Slide 38: An Example
Let’s find a mask to clear bits 2, 3 and 5 in an 8-bit byte
  Since we have to clear bits, we need an AND instruction
  The mask is the 8-bit byte that we AND against the data
For the AND instruction, we code the mask in binary
  Hex is OK too

## Slide 39: The Instruction
Here is a picture of the bits
The mask is (in binary) 11010011
Suppose the data is in the byte x
The instructions are
  moveb $0b11010011, %al
  andb x, %al
The ax register now contains the result

## Slide 40: The OR instruction 02

## Slide 41: Doing the Same for OR
OR matches | in C++
  | is like ||
  | is an operator, || is for comparisons
The bit rules for OR are
0 OR 0 = 0
0 OR 1 = 1
1 OR 0 = 1
1 OR 1 = 1

## Slide 42: An Example
Let’s try a problem

## Slide 43: The Takeaway for OR
The key item to notice for OR is this
0 OR 1 = 1 0 OR 0 = 0
1 OR 1 = 1 1 OR 0 = 1
ANYTHING OR 1 = 1
ANYTHING OR 0 = itself
This means that ORing against 1 changes bits to 1
We call this setting bits

## Slide 44: An Example
Let’s find a mask to set bits 2, 4 and 7 in an 8-bit byte
  Since we have to set bits, we need an OR instruction
  The mask is the 8-bit byte that we OR the data against
Like the AND instruction, we code the mask in binary
  Again, hex is OK too

## Slide 45: The Instruction
Here is a picture of the bits
The mask is (in binary) 10010100
Suppose the data is in the byte x
The instructions are
  moveb $0b10010100, %al
  orb x, %al
The al register now contains the result

## Slide 46: Syntax
The syntax is the same for AND, OR, and XOR
  XOR will be discussed later
The syntax is
  ORW %ax, $0xFFFF
  ANDB %ah, $0b11010111
  ORB %ah, %bh
  ANDW %ax, x

## Slide 47: Other Logical Instructions 03

## Slide 48: The NOT, NEG Instructions
The NOT instruction does a 1’s complement
  This is what I refer to as “flipping the bits”
The syntax is notl %eax
You can also code notl x
The NEG instruction does a 2’s complement
  This gives the negative of the number
The syntax is negl %eax
You can also code negl x

## Slide 49: The XOR Command
This is in the same category as AND and OR
Here are the bit rules for XOR
  0 XOR 0 = 0
  0 XOR 1 = 1
  1 XOR 0 = 1
  1 XOR 1 = 0
Notice that XOR is
  0 if the bits are the same
  1 if the bits are different

## Slide 50: An Example
Let’s try some XOR problems

## Slide 51: Two XOR Takeaways
If you XOR two identical values, the result is 0
Suppose
  You XOR a value against a mask
  You then XOR the result against the same mask
You end up where you started
  This is because 0 XOR 0 = 0, and 1 XOR 0 = 1

## Slide 52: The Shift Instructions 04

## Slide 53: Two Plain Shift Instructions
SHLB $3,%ah
  This means to shift ah left 3 bits
  This moves every bit in ah left 3 positions
  Bits moved out of the register are lost
  0 is moved into all “empty” positions
There is also a right shift (SHR)
  The syntax is the same as SHL

## Slide 54: Other Versions of the Shift Instruction
SHL %ah
  This means to shift ah left 1 bit
  It’s a shorter version of the instruction
There is a similar format for the SHR instruction
There is yet another version of the shift instructions
This is SHL %cl, %ax
  The %ax can be any valid operand
  The cl register must contain a number less than 6

## Slide 55: Two Arithmetic Shift Instructions
SALB $3,%ah
  This means to shift ah left 3 bits
  This is actually the same as SHLB $3,%ah
There is also a right shift (SAR)
  A right shift by n bits is an integer divide by 2n
  But, this shift sign-extends
    The A stands for arithmetic

## Slide 56: The Shift Instructions and Math
A left shift is the same as multiplication
Shifting left n bits is like multiplying by 2n
A right shift is like division
Shifting right n bits is like dividing by 2n

## Slide 57: The Rotate Instructions
Rotating is different from shifting
Bits that are shifted out of one “side” of a register or memory location are moved into the other ”side”
For example
  Suppose al contains 1010111
  You execute ROR $3,%al
  Then al contains 1111010
There is also a ROL (Rotate left)

## Slide 58: Section 3
Floating Point:
Storage and Instructions

## Slide 59: Floating Point Data 01

## Slide 60: How is Floating Point Data Stored?
Wait! Not the glasses again! 

## Slide 61: Interpreting Storage As Floating Point
I will talk about the usual 32-bit floating point format
Here is a picture of a floating point number in 32 bits

## Slide 62: 2’s Complement was quite involved. Are we going to do it again?
Luckily, we aren’t. 
But you see that there still is a sign bit
We first set the sign bit
Then we store the number
The number part of positive and negative numbers is stored in exactly the same way
  We store the absolute value
The only way to differentiate positive and negative numbers is to look at the sign

## Slide 63: On to the Mantissa
The mantissa is the number itself
The first step in storing the number is to convert it to binary
We already know how to convert a whole number to binary
What about the fractional part?
So, to do this, we break the problem into two parts:
  Convert the whole number part
  Convert the fractional (decimal) part

## Slide 64: Converting a Fraction to Binary
I will now focus on the fractional part
I will focus on easy cases
  There is a technique similar to the long division technique, that uses multiplication
  If you want to learn the technique, check with me outside of class
For now, I will start by listing these facts
  0.12 = 0.510 or 1/2
  0.012 = 0.2510 or 1/4
  0.0012 = 0.12510 or 1/8

## Slide 65: Using Those Facts
Start with 0.5 in the list
Compare it to your fraction
If your fraction is greater than or equal to 0.5
  Subtract 0.5 from your number
  Write down the binary version of 0.5
Repeat this for 0.25 and 0.125, stopping when the result is 0
Add up the binary numbers
Some examples follow

## Slide 66: Converting 3.25 to Binary
The whole number part is 310, which is 112
The fraction is 0.25
It’s less than 0.5, so skip this number
It’s equal to 0.25, so
  0.25-0.25 = 0
  I write down 0.01 (binary)
The answer is 0, so the converted fraction is 0.01
The final answer is 11.01

## Slide 67: Converting -12.75 to Binary
Convert the whole number part
  1210 = 11002
Convert the fraction
  0.75 is greater than 0.5, so
    0.75-0.5 = 0.25
    Write down 0.1 (binary)
  0.25 is equal to 0.25, so
    0.25-0.25=0
    Write down 0.01 (binary)

## Slide 68: Finishing the Conversion
Add up the numbers you wrote down
0.1 + 0.01 = 0.11
  This is binary math!
So, 12.7510 = 1100.112
Later on, we will remember that this was negative

## Slide 69: Normalizing the Number
Now, we rewrite the number in (binary) scientific notation until there is only one 1 on the left side of the decimal point
3.2510 = 11.012 = 1.101 * 21
12.7510 = 1100.112 = 1.10011 * 23
  When we store this, we will delete that 1 to the left of the decimal point
Then we add 127 to the exponent
  We call this biasing the exponent by 127

## Slide 70: Viewing the Bits
Now we store the pieces
3.25 is stored as + 128 101, which is
-12.75 is stored as - 130 10011, which is

## Slide 71: Floating Point Math
Floating point math is a bit different
It uses a floating point stack
  You can also use memory
It’s a bit different from integer math
Some examples follow

## Slide 72: Code Specifics
You can declare a floating point constant
You can push a floating point number onto the stack
You can add the top two numbers on the stack and push the result

## Slide 73: A Sample Program
The book has a sample program
You should look at it
Like all the programs in the book, you can type it in and run it
You can use the debugger to follow it

## Slide 74: CREDITS!
CREDITS: This presentation template was created by Slidesgo, including icons by Flaticon, and infographics & images by Freepik.